## Slide 1: Project Seminar, 2024
Land Cover Classification based on Multiscale Time Series of Satellite and Aerial Images
Supervisors:
M.Sc. Hubert Kanyamahanga,
Dr.-Ing. Mareike Dorozynski
Students:
Mahsa Ghandali
Sunanda Menon
Shiva Timilsina
Mohammad Mansouri
Suman Khanal

## Slide 2: Overview
Introduction
Methodology
- Baseline architecture
- Self-Supervised Learning (SSL)
Experiments
- Dataset and experimental setup
Results
Conclusion

## Slide 3: Introduction
Motivation
- To achieve high quality Land Cover (LC) predictions.
- Advantage of combining temporal and spatial information.
- Land Cover Classification for Hameln region.
Aerial image
Satellite Image Time Series (SITS)

## Slide 4: Introduction
Challenges
- Integrating multi sensor data.
- Availability of very few high-quality training labels.
Our approach
- Self-Supervised Learning (SSL)
Large unlabelled data for pre-training and small labelled data for fine-tuning.
SSL has been shown to outperform Supervised Learning method in the literature.

## Slide 5: Baseline architecture (Supervised learning)
Temporal VIT
Pixel-wise predictions
40
512
512
512
GSD: 10m
40
GSD: 0.2m
512
U-Net
Encoder
Decoder

## Slide 6: Self-Supervised Learning (SSL)
​
​
UNLABELED Dataset
Backbone
Projection Head
Self-supervised pre-training
2. Supervised fine-tuning
LABELED Dataset
Segmentation Head

## Slide 7: Contrastive Learning
A Simple Framework for Contrastive Learning of Visual Representations (SimCLR)
Transformation: t , t`
Views: xi , xj
Encoder: f ( . )
Feature map: hi , hj
MLP(Projection): g( . )
Feature Map(MLP): zi , zj

## Slide 8
Xi
Xi
Xj
Xj
SITS
Aerial
Temporal ViT
Temporal ViT
Hi
Hj
Fully Connected
Contrastive Learning
Zi
Zj
Fully Connected
Fully Connected
Fully Connected
f ( . )
f ( . )
Transformation : t , t`
Views: xi , xj
Encoder : f ( . )
Feature map : hi , hj
MLP(Projection) : g( . )
Feature Map(MLP): zi , zj
2048
128
2048
128
ReLU
ReLU
Projection Head (g)
t
t`
U-Net Encoder
U-Net Encoder

## Slide 9: Supervised fine-tuning
SITS
Aerial
Temporal ViT
Segmentation Head
U-Net Encoder
U-Net Decoder
Pixel-wise predictions

## Slide 10: Positive and Negative pair generation
Data Augmentation
Geometric and Radiometric transformation
Cropping randomly and resizing (20%)
Gaussian blur
Erasing part of image
Brightness and contrast changes
Simulation of different lighting condition
Aerial
SITS

## Slide 11: Contrastive learning loss
l i, j : Loss for the image positive pair (i, j)
sim (zi , zj ) : Similarity measure between feature vectors zi​ and zj​ (cosine similarity)
τ: Temperature parameter that scales the similarities
2N: Total number of images in the batch
1[k≠i] : Indicator function that equals 1 if k≠i, and 0 otherwise
exp(⋅) : Exponential function

## Slide 12: Data
Pre-training
Fine-Tuning
9322 Patches
2077 Patches
Hameln:

## Slide 13: Data
Aerial
Mono-Temporal
GSD: 0.2 m
Channels: 4(R,G,B,IR)
Patch size: 512*512 pixels
Hameln:
SITS
Feb - Nov
GSD: 10 m
Channels: 10
Patch size: 40*40 pixels
length of time series:8
Time series
Aerial patch

## Slide 14: Data
FLAIR #2
Open-source dataset (France)
Task: LC classification
Contains aerial and SITS images
Labelled dataset
50 areas in France

## Slide 15: Experiments
SSL
Supervised Learning
# | Pre-Training Data | Pre-Training Epochs | Fine-tuning Data | Fine-tuning Epochs | Batch | Temp
1 | Baseline (FLAIR 2) | 30 | Baseline | 5 | 16 | 0.1
2 | Hameln | 40 | Hameln | 20 | 16 | 0.1
3 | Hameln | 40 | Hameln | 20 | 8 | 0.7
# | Dataset | Epochs
1 | Baseline | 30
2 | Hameln | 50

## Slide 16: Setup
Optimiser: Stochastic gradient descent with learning rate of 0.001
Supervised fine-tuning : Cross entropy loss with adjusted weights for imbalance class handling.
Batch size: 8, 16
Projection head: 2-layers FCN, ReLU activation
Temperature parameter : 0.7, 0.1
Evaluation metrics: IoU

## Slide 17: Results
# | Buildings | Underground working | Loose material | grass | reed | crop | Deciduous trees | Coniferous trees | grove | shrubbery | Running water | Standing water
SSL1 | 63.00 | 38.07 | 0.00 | 10.58 | 19.20 | 30.00 | 33.04 | 3.01 | 0.00 | 0.00 | 0.00 | 0.00
SSL2 | 73.00 | 39.00 | 0.00 | 15.00 | 25.6 | 37.22 | 35.80 | 6.80 | 0.00 | 0.00 | 0.00 | 0.00
SUP | 72.00 | 40.00 | 0.00 | 13.53 | 20.4 | 43.50 | 35.80 | 9.50 | 0.00 | 0.00 | 0.00 | 0.00
# | Buildings | Pervious surface | Impervious surface | Bare soil | water | coniferous | deciduous | brushwood | vineyard | herbaceous vegetation | land | plowed land
SSL | 53.00 | 32.00 | 52.00 | 21.00 | 65.00 | 34.00 | 60.00 | 17.00 | 40.00 | 36.00 | 43.0 | 32.0
SUP | 77.80 | 45.90 | 68.00 | 33.80 | 82.20 | 29.50 | 64.7 | 21.4 | 56.1 | 41.00 | 49.2 | 37.60
Hameln
Baseline

## Slide 18: Results
Dataset and method | mIoU | OA
Baseline SL | 50.63 | 66.80
Hameln SL | 19.56 | 47.74
Baseline SSL | 40.91 | 61.09
Hameln SSL | 16.41 | 38.42
Hameln SSL | 19.37 | 41.45

## Slide 19: Limitations
Very few labeled images (2077) available.
Manual quality check of produced annotations.
Problem with batch size
    Our batch size : 8
    Reference paper minimum batch size 256

## Slide 20: Conclusion
Implemented multimodal SSL on existing baseline.
Utilized the unlabelled data for model pre-training.
Supervised learning has better mIoU and OA than SSL in our experiments.
There is room for improvements.

## Slide 21: Outlook
Getting more training data with labels.
Using method that does not rely on negative samples or require few negative samples.
Fusion module can be improved (Attention based)
    Squeeze-Excitation
    Residual-Excite

## Slide 22: References
Garioud, Anatol, Apolline De Wit, Marc Poupée, Marion Valette, Sébastien Giordano, and Boris Wattrelos. "FLAIR: French Land cover from Aerospace ImageRy." arXiv, 2023. https://arxiv.org/abs/2305.14467.
Ting Chen, Simon Kornblith etc, A Simple Framework for Contrastive Learning of Visual Representations https://arxiv.org/abs/2002.05709
Linus Scheibenreif Jo¨elle Hanna Etc, Self-supervised Vision Transformers for Land-cover Segmentation and Classification https://ieeexplore.ieee.org/document/9857009
Yongshuo Zong, Oisin Mac Aodha Etc, Self-Supervised Multimodal Learning: A Survey https://arxiv.org/pdf/2304.01008